## Slide 1: Chapter 7: Network Concepts and Communications
Going online to do everything from banking to buying groceries, just a fad or is it here to stay?

## Slide 2: Network Concepts and Communication
In this lecture:
  What can be done online?
  How are computers connected?
  What are the physical properties of networks?
  How does a computer communicate with a network?
  Can all computers talk to each other?
  How does TCP/IP work?

## Slide 3: Introduction: “Everything is Connected to Everything”
Going online: Connecting to a collection of interconnected computers on a network.
  Do banking.
  Pay bills.
  Buy groceries.
  Book vacation travel.
  Send messages.
  Participate in discussions.
  Do research.
  Play games.
Network: A collection of computers, display terminals, printers, and other devices linked either by physical or wireless means.

## Slide 4: Introduction: “Everything is Connected to Everything”
Seeds of Networking
  1966: ARPA (Advanced Research Projects Agency) State Defense Department’s research organization.
    Focused major development effort on computer networking.
    ARPA’s Goal: To promote research in advanced future technologies by funding university and industry research proposals.
      Distributed communication system
      Enable research communication
      Enable dissimilar computers to share information
      Reroute information automatically
      Act as a network of networks; internetworking
  Result: Thousands of databases became available to the public.

## Slide 5: The Internet: Struggling to Maturity
ARPA intended to sell off the ARPAnet to an academic or corporate consortium.
  Before the sale, federal rules required the Defense Department to determine if ARPAnet was needed for national defense.
  ARPAnet was transferred to the Defense Communications Agency in 1975.
  Only about 15 universities were given access to the network.
1980: National Science Foundation started CSnet
  Purpose: To provide a resource-sharing network opportunity to computer science research at all universities.
  Used TCP/IP protocol.

## Slide 6: The Internet: Struggling to Maturity
CSnet fueled interest in creating a more comprehensive network to link all scientific communities (not just CS)
  NSF couldn’t fund such an expensive project.
    Backbone: NSF built a very fast connection between 5 supercomputing centers linking them all together.
    Each region surrounding each center would develop its own community network.
    NSF allowed the regional community networks exclusive use of the backbone.

## Slide 7: The Internet: Struggling to Maturity
1983: ARPAnet split.
  Converted from Network protocol to TCP/IP protocol.
  Part remained ARPAnet: universities, research institutes.
  Part became Milnet: non-classified military information.
  By 1989, ARPAnet was costing $14 million per year to keep up and running.
1989: majority of ARPAnet switched to NSF’s backbone.
  ARPAnet sites were connected to the NSF backbone through the regional community networks.
NSFnet became what is known as the Internet.
Early 1995: “Information Superhighway.”

## Slide 8: Introduction: “Everything is Connected to Everything”
Computer Networking
  Internet: A world-wide network connecting millions of computer networks for the purpose of exchanging data and communications using special rules of communication.
  internet: (lower case i) Any network connecting two or more computer networks.
The World Wide Web <> the Internet
  WWW exists on the Internet
  Internet includes the basic technology of interconnecting networks, WWW is an application on the Internet
    Just like telnet, ssh, ftp, etc.

## Slide 9: Communication Basics of Networks
Types of connections of computers into networks: Physical versus Wireless connections
  The first type: The Physical Connection.
    Physically connect computers together.
      Use of wires or optical cables.
      The connections are called network links.
    Three most common physical links:
      Twisted pair
      Coaxial cable
      Fiber-optic cable

## Slide 10: Communication Basics of Networks
Twisted pair
  Two wires twisted together.
    Makes them less susceptible to acting like an antenna and picking up radio frequency information or appliance noise.
    Cat1 to Cat5e
    Shielded, Unshielded, use RJ-45 connector
      10BaseT or 100BaseT network
  Telephone company uses twisted-pair copper wires to link telephones.

## Slide 11: Communication Basics of Networks
Coaxial cable
  Also two wires:
    One of the wires is woven of fine strands of copper forming a tube.
    The wire mesh surrounds a solid copper wire that runs down the center.
    Space between has a non-conducting material.
    Makes them more impervious to outside noise.
  Uses BNC connector, 10Base2 or 10Base5

## Slide 12: Communication Basics of Networks
Fiber-optic cable
  Light is electromagnetic.
  Can transmit more information down a single strand.
    It can send a wider set of frequencies.
  Each cable can send several thousand phone conversations or computer communications.
  Single Mode, Multimode, Step Index Multimode

## Slide 13: Communication Basics of Networks
Second type of connections of computers into networks: Wireless connections
  The link is made using electromagnetic energy that goes through space instead of along wires or cables.
  Three types of wireless communications commonly used in networking:
    Infrared
    Radio frequency
    Microwave

## Slide 14: Communication Basics of Networks
Infrared
  Commonly used in TV and VCR remote controls.
  Use infrared frequencies of electromagnetic radiation that behave much like visible light.
  Must be in the line of sight.
  Often used to connect keyboards, mice, and printers.
  Relatively slow due to protocol

## Slide 15: Communication Basics of Networks
Radio frequency
  Uses radio frequencies.
    Function even though line of sight is interrupted.
  Book says: Not commonly used because of the possible interference from other sources of electromagnetic radiation such as old electric drills and furnace motors.
  Not anymore! RF becoming very popular
    Wireless networking is becoming a huge market
    New standards, 802.11
    2.4Ghz unlicensed ISM band
    Range of typically ~300 feet
    Security concerns

## Slide 16: Communication Basics of Networks
Microwave
  Often used to communicate with distant locations.
  Must be line of sight.
  Satellite communications use microwaves.
    ~22,000 mile orbit

## Slide 17: Communication Basics of Networks
Properties of Transmission
  Five basic properties of both the physical and wireless links:
  1. Type of signal communicated (analog or digital).
  2. The speed at which the signal is transmitted (how fast the data travels).
  3. The type of data movement allowed on the channel (one-way, two-way taking turns, two-way simultaneously).
  4. The method used to transport the data (asynchronous or synchronous transmission).
  5. Single channel (baseband) and multichannel (broadband) transmission.

## Slide 18: Communication Basics of Networks
1. Type of signal communicated (analog or digital).
  Analog: Those signals that vary with smooth continuous changes.
    A continuously changing signal similar to that found on the speaker wires of a high-fidelity stereo system.
  Digital: Those signals that vary in steps or jumps from value to value. They are usually in the form of pulses of electrical energy (represent 0s or 1s).

## Slide 19: Communication Basics of Networks
2. The speed at which the signal is transmitted (how fast the data travels).
  In digital systems: Speed is measured in...
    Bits per second (bps).
      The number of bits (0’s and 1’s) that travel down the channel per second.
    Baud rate
      The number of bits that travel down the channel in a given interval.
      The number is given in signal changes per second, not necessarily bits per second.

## Slide 20: Communication Basics of Networks
MODEM - MOdulator DEModulator
  Outgoing: Converts binary data from computer (digital) into telephone compatible signals (analog).
  Incoming: Converts telephone signal (analog) into binary data for the computer (digital).
  Can be an external or internal device (usually a “card”).

## Slide 21: Communication Basics of Networks
Speed of Signal: Sample bps and baud rate speeds.
300 bps (=300 baud) Painfully slow to the college-level reader
1200 bps (=1200 baud) Good reader can keep up
2400 bps (=2400 baud) A speed reader would get the general idea
9600 bps (=9600 baud) Impossible to read
14.4 K bps (not measured in baud) 14,400 bps - 10 to 20 sec. wait for graphics
28.8 K bps Minimum desired for WWW
(5 to 10 sec. wait for graphics)
56 K bps Efficient speed for WWW.
These speeds are restricted to the maximum speed of the modem at the
other end of the connection.

## Slide 22: Communication Basics of Networks
3. The type of data movement allowed on the channel.
  Simplex transmission - One way transmission.
  Half-duplex transmission - Flows only one way at a time.
  Full-duplex transmission - Two-way transmission at the same time.

## Slide 23: Communication Basics of Networks
4. The method used to transport the data.
  Two types of data transmission, each requiring a different device to interface with the network.
  Asynchronous transmission -
    Information is sent byte by byte.
    Cheaper and more commonly used mdem
  Synchronous transmission -
    Data is sent in large blocks rather than in small pieces.
    Preceded by special information, concerning error detection and block size.
    Network interface card (NIC)

## Slide 24: Communication Basics of Networks
5. Multiplexing - Single channel versus multichannel transmission
  Channel - A path of a signal.
  Single channel - Capable of only sending/receiving one signal at a time.
    Phone line: Single line = single phone call at a time.
  Multichannel - Capable of more than one channel at a time.
    Fiber-optic cable, microwaves, Satellite transmissions.
    Multichannel transmission could typically be used instead as one single channel medium with capacity equal to the sum of the individual channels
      Need to figure out optimal way to split up the channel

## Slide 25: Communication Basics of Networks
How is it possible to measure the capacity of communications links?
  Bandwidth: Digital
    Number of bits per second (bps) that can be sent over a link.
    The wider the bandwidth, the more diverse kinds of information can be sent.
    Simplest is voice, most sophisticated is moving videos.
  Bandwidth: Analog
    The difference between the highest and lowest frequencies that can be sent over an analog link (like phone lines).
    Measurement is given in cycles per second, or hertz (Hz).
  For both: The wider the bandwidth, the more information can flow over the channel.

## Slide 26: Communication Basics of Networks
Mbps = megabytes per sec. (millions) Gbps=Gigabytes per sec. (billions)
Typical cable bandwidths used in local area networks.
Cable: Typical Bandwidth:
Twisted Pair 10 to 100 Mbps
Coaxial Cable 10 to 100 Mbps
Fiber-optic cable 100 to 200 Mbps
The bandwidths of different services offered by a telephone company:
Service: Bandwidth
ISDN 64 Kbps/channel
T1 1.544 Mbps
T3 44.736 Mbps
STS-1 51.840 Mbps
STS-3 155.250 Mbps
STS-12 622.080 Mbps
STS-24 1.244160 Gbps
STS-48 2.488320 Gbps

## Slide 27: The Physical Organization of Networks
Node: The generic name given to all devices hooked up to a network.
  Each node must have a unique address assigned to them by the network.
  Networks are either direct-connected or those that are not directly linked.
    Direct-connected network: Those whose nodes have direct connections through either physical or wireless links.
      Point-to-point: Simplest version of direct-connected network. Connecting two computing systems.
        Example of point to point: Home to ISP.
    Example of a network that is not directly linked: Internet.

## Slide 28: The Physical Organization of Networks
The bus network -
  A continuous coaxial cable to which all the devices are attached.
  All nodes can detect all messages sent along the bus.
The ring network -
  Nodes linked together to form a circle.
  A message sent out from one node is passed along to each node in between until the target node receives the message.
Linking nodes:
Both of these topologies are uncommon today

## Slide 29: The Physical Organization of Networks
The star network -
  Each node is linked to a central node.
  All messages are routed through the central node, who delivers it to the proper node.
  Most common today
The tree network - (hierarchical network)
  Looks like an upside-down tree where end nodes are linked to interior nodes that allow linking through to another end node.
Linking nodes:

## Slide 30: The Physical Organization of Networks
The fully connected network -
  All nodes are connected to all other nodes.
  Typically too expensive to implement, need n(n-1)/2 connections for n nodes
Internetworking -
  Connecting together any number of direct-connected networks.
  The largest: Internet.
Linking nodes:

## Slide 31: Hardware Architecture of Networks
Types of hardware used to create networks:
Hub A device that repeats or broadcasts the network stream of information to individual nodes ( usually personal computers)
Switch A device that receives packets from its input link, and then sorts them and transmits them over the proper link that connects to the node addressed.
Bridge Transparently links two local networks that have identical rules of communication.
Gateway A link between two different networks that have different rules of communication.
Router A node that sends network packets in one of many possible directions to get them to their destination.

## Slide 32: Star Network via Hub
Workstation
Hub

## Slide 33
Bridge LAN / Backbone Design

## Slide 34
Switched LAN / Backbone Design

## Slide 35: Routers – Connect Networks

## Slide 36: The Physical Organization of Networks
Categorizing networks according to size:
  DAN (Desk Area Network)
  LAN (Local Area Network)
  MAN (Metropolitan Area Network)
  WAN (Wide Area Network)

## Slide 37: The Physical Organization of Networks
DAN (Desk Area Network)
  Making all components of a desktop computer available to other computers on the network.
    CPU - Unused computing power can be used by other computers on the network.
    Hard Disk - Items stored can be accessed by others or items may be placed on the hard drive from other computers.
    Video Display - Alert messages can be sent to the computer’s display.
    Other items - Other devices connected to the computer might be needed by others connected to the network.

## Slide 38: The Physical Organization of Networks
LAN (Local Area Network)
  A collection of nodes within a small area.
  The nodes are linked in a bus, ring, star, tree, or fully connected topology network configuration.
  Benefits of LANs:
    Sharing of hardware resources.
    Sharing of software and data.
    Consolidated wiring/cabling.
    Simultaneous distribution of information.
    More efficient person-to-person communication.

## Slide 39: The Physical Organization of Networks
MAN (Metropolitan Area Network)
  Consists of many local area networks linked together.
  Span the distance of just a few miles.
  Sometimes called a BN (Backbone Network)
WAN (Wide Area Network)
  Consists of a number of computer networks including LANs.
  Connected by many types of links.

## Slide 40: Software Architecture of Networks
Problem:
  Connect several different machines running different operating systems (Windows, OS/2, MacOS, UNIX, VMS...)
  Now, try to: send email, data or files between them.
Solution:
  Create a standardized set of rules, or protocols, that, when followed, will allow an orderly exchange of information.
  A collection of these programs is called a protocol suite.
    Must be on all computers or nodes in the network.
    In order to send data over the network, the necessary programs must be executed.
  Network’s architecture: The protocol suite and the general scheme that guides the network’s rules.

## Slide 41: Software Architecture of Networks
Problem: Collisions of information are caused by two computers simultaneously attempting to send information to the network.
Solution: Different networks have different protocol suites:
  Apple Computer’s LocalTalk Protocol - Permission must be granted before information can be sent along the network.
  Token-Ring Protocol (IBM and others) - A token is “picked up” by a node signifying that a message is about to be sent, the computer sends the message, then, replaces the token so that others can use the network.
  Ethernet Protocol (Xerox and others) – CSMA/CD
    “Listen” for quiet line; then send message
    Collision occurs with simultaneous messages
    Must wait and resend

## Slide 42: Token Ring Operation
B
(1)
A
C
Token
B
(2)
A
Message
For
"C"
C
B
(3)
A
C
C
C
B
(4)
A
C
B
(5)
A
C
B
(6)
A
C
C
C

## Slide 43: How Does the Internet Work?
Packet-Switching Technology
Connecting Independent Networks
TCP/IP
Internet Services
The World Wide Web
Notes: <number>
<footer>
<header>
The underlying technology to the Internet is a high-speed central network called the backbone. It is a hierarchical structure with smaller networks connected to the backbone. It is analogous to the Interstate highway system with state highways connecting to the interstates and so on. As with the highway system, it must be shared with others and users must agree to follow certain rules when using the system.

## Slide 44: Packet-Switching Technology
Data sent in small standard sized chunks called “packets”
Packets have headers with addresses of sending and receiving computers
Users take turns sending packets
Packets reassembled by the receiver
Notes: <number>
<footer>
<header>
To minimize delays, network technologies limit the amount of data (number of packets) a computer can transfer on each turn.
If only one computer needs to use the network, it can send data continuously. As soon as another computer needs to send data, turn-taking begins.

## Slide 45: Packet Switching
1st packet from A to C
1st packet from B to D
2nd packet from A to C
2nd packet from B to D
3rd packet from A to C
A
B
C
D
C
Shared Network System
D
C
D
C

## Slide 46: Connecting Independent Networks
Router: fundamental building block of the Internet
  Has a processor, memory, and network interface, its own specialized software
  Connects LANs to backbone WANs
  Forwards packets from one network to another
  Determines best routes for packets to travel
Notes: <number>
<footer>
<header>
Routers are special-purpose computers with no software.
Routers are the means through which thousands of LANs and WANs are interconnected. A backbone network manages the bulk of network traffic and typically uses a higher-speed protocol than the individual LAN segments.
To gain access to the Internet, organizations generally connect a router between one of its own networks and the closest Internet site. Individuals use telephone dial-up services to connect to a computer or network that is connected to the Internet.

## Slide 47: Routers Enable Different Paths between Networks
Router
Path 1
Path 6
Path 5
Path 3
Path 4
Path 2
Network A
Network B
Network C

## Slide 48: TCP/IP
Transmission Control Protocol
  Breaks information into data packets
  Reassembles packets when received
  Checks for lost packets
Internet Protocol
  Each computer given a unique IP address, e.g. 137.224.44.12
  IP address corresponds to an application level “Name”, e.g. www.yahoo.com
  Name shows up in URLs, Email…
    http://www.yahoo.com/somepage/on/yahoo/index.html
    afkjm@uaa.alaska.edu
Notes: <number>
<footer>
<header>
Organizations use diverse network technologies that may not be compatible with the technologies of other organizations. Because so many different networks are connected, they must have a common protocol to communicate. The protocol of the Internet is TCP/IP.
TCP control s the packets. IP controls the addressing of individual machines. Packets travel independently to their destination, sometimes following different paths and arriving out of order. The destination computer uses TCP to reassemble the packets based on their identification and sequencing information.
Every computer that uses the Internet must run IP software. The IP defines how a packet must be formed and how a router must forward each packet. TCP helps guarantee delivery of the packets.

## Slide 49: Basics of Internet Communication
Messages broken into datagrams, also known as packets:
Sequence Number
Source Address
Destination Address
Data Size
(Other fields)
Data
34
128.120.56.214
199.237.80.7
7
…
hi mom
TCP/IP : Transmission Control Protocol / Internet Protocol

## Slide 50: Packet Routing
Packets may travel different routes to reach their destination
Sequence number used to put data back in the original order

## Slide 51: High Level Software Architecture
Different Layers in the “Stack”
  Application
    Programs like web browsers, servers,
    Protocols such as ftp, ssh, httpd, html
  Transport
    Keeps track of a session, breaks data into packets, error checking
    Protocols such as TCP or UDP
  Internet
    Routes messages to their destination
    Protocols such as IP
  Data Access or Data Link
    Controls physical hardware
    Protocols such as Ethernet, PPP
  Physical
    Physical medium, twisted pair, fiber, radio, etc.

## Slide 52: Software Architecture of Networks
The Architecture of the Internet
FTP
HTTP
NV
TFTP
TCP
UDP
IP
Network #1
Network N
Network #2
Application
Transport
Internet
Data Link
Physical

## Slide 53: Internet Naming Conventions
Names of computers use the following convention for domains
hostname.subdomain.domain.type
  type : Organization status
  domain : Registered ICANN name
  Subdomain : optional hostname
  Hostname : Name of the machine

## Slide 54: Common Types
.edu - Educational
.gov - Government
.org - Nonprofit organizations
.net - Internet service providers, backbone
.country - Two letter country code, e.g. .jp for Japan, .us for United States, .to for Togo
New names recently approved:
  .aero, .biz, .museum, .info

## Slide 55: Hierarchy of Names - DNS
Routers are based on IP address (e.g. 134.114.140.34), not the English-like domain name!
DNS = Domain Name Server system
  Way to translate from domain name to IP address
Tree-based hierarchy, with .org, .com, .edu, and .gov at the top of the tree

## Slide 56: DNS - Finding IP Addresses
Each computer on the network has an IP address
  0.0.0.0 to 255.255.255.255
  Some of these are reserved; 127.0.0.l, 192.168.x.x
DNS name servers map names to IP addresses
  distributed database on the network

## Slide 57: Network Example: Traceroute
Traceroute: A program that allows the the tracing of packets over the Internet or any network using TCP/IP protocol.
  Uses a special number - TTL (Time to Live) - contained in a place at the beginning of each packet sent over the network.
    The number is originally set to 255.
    Each time it is received by a router, it decrements by 1.
    If the TTL number becomes 0 before reaching its destination, the router where this happened sends back an error message (time exceeded) with the address of the router.
      Stops messages from circulating forever.

## Slide 58: Tracing the router hops…
On mazzy: /usr/sbin/traceroute <dest> On Windows: tracert <dest>
Tracing route to www.alaska.net [209.112.131.196] over a maximum of 30 hops:
1 431 ms 440 ms 421 ms uaa-du-02.alaska.edu [137.229.98.66]
2 350 ms 341 ms 300 ms r98-99-e1.alaska.edu [137.229.98.99]
3 361 ms 340 ms 381 ms swf-7507-1 [137.229.254.21]
4 300 ms 341 ms 300 ms m40 [137.229.2.1]
5 290 ms 321 ms 320 ms uacore1-ge-0-0-0-0.pnw-gigapop.net [198.32.40.129]
6 411 ms 401 ms 390 ms westincore1-so-0-1-0-0.pnw-gigapop.net [198.48.91.33]
7 431 ms 380 ms 441 ms westinnsp2-GE1-0.pnw-gigapop.net [198.32.170.17]
8 631 ms 440 ms 461 ms p1-1-2-2.a07.sttlwa01.us.ra.verio.net [204.203.3.1]
9 591 ms 640 ms 461 ms ge-6-2-0.r03.sttlwa01.us.bb.verio.net [129.250.28.1]
10 521 ms 500 ms 421 ms p4-5-0-0.r06.plalca01.us.bb.verio.net [129.250.3.89]
11 461 ms 450 ms 511 ms p4-6-0-0.r01.snjsca03.us.bb.verio.net [129.250.2.198]
12 621 ms 681 ms 620 ms p4-1-0-0.r00.lsanca01.us.bb.verio.net [129.250.2.114]
13 611 ms 661 ms 621 ms p1.att.r00.lsanca01.us.bb.verio.net [129.250.9.34]
14 601 ms 541 ms 531 ms gbr3-p50.la2ca.ip.att.net [12.123.28.130]
15 481 ms 421 ms 560 ms gbr4-p20.sffca.ip.att.net [12.122.2.69]
16 371 ms 420 ms 401 ms gbr3-p30.st6wa.ip.att.net [12.122.2.198]
17 400 ms 481 ms 481 ms gbr2-p10.st6wa.ip.att.net [12.122.5.166]
18 421 ms 421 ms 410 ms gar1-p370.st6wa.ip.att.net [12.123.44.62]
19 521 ms 561 ms 540 ms 12.123.203.1
20 440 ms 441 ms 501 ms 12.124.174.6
21 561 ms 440 ms 461 ms www.alaska.net [209.112.131.196]
21 hops from Anchorage to Anchorage!

## Slide 59: Network Security
Security of a Network
  Enterprise and intranet networks: Corporations, government agencies, and other organizations have created their own internal networks.
    Firewall: A set of programs that monitor all communication passing into and out of a corporation’s intranet.
      Helps prevent, but doesn’t eliminate, unauthorized access.
Upgrade and Apply Patches Often!
  Avoid intrusions via known bugs or holes
  Lots of worms, DOS (denial of service) attacks, known exploits to compromise security