## Slide 1: CS 442 Data Communications
Introduction

## Slide 2: What is this course about?
Networking: system for connecting computer using a single transmission technology
Internet: set of networks connected by routers that are configured to pass traffic among any computers attached to networks in the set
Data transmission - media, data encoding
Packet transmission - data exchange over a network
Internetworking - universal service over a collection of networks
Network applications - programs that use an internet

## Slide 3: First, a Brief History of the Internet
ARPAnet (Advanced Research Projects Agency) in 1969
Early computers were expensive
  Large footprint , Centralized
Programs took a long time to run
Couldn't afford to put computers everywhere
Distributed communication system
Enable research communication
Enable dissimilar computers to share information
Reroute information automatically
Act as a network of networks; internetworking
Originally just 4 sites!

## Slide 4: Original ARPANet Sites

## Slide 5: ARPANet in 1972

## Slide 6: More Internet History
1975 – ARPAnet splits into MILNET and NSFNet
1979 – Usenet/UUCP over modems
1982 – DARPA uses TCP/IP over Ethernet
1983 – BSD Unix over Ethernet
1984 – DNS
1988 – Morris worm
1993 – Web starts to take over
  www.whitehouse.gov
1994 – Big business online booms

## Slide 7: Evolution of the Internet
Commercial networks
  AOL, Compuserve, et. al. grow in the 80’s, incorporated into Internet in 90’s
NSFNet shut down in 1995 in favor of NAP structure, commercial backbones

## Slide 8: Exponential Growth # Hosts (Computers connected)

## Slide 9: # of Web Sites

## Slide 10: Creation of the WWW
Technologies required: HTML, Browser
HTML : Designed by Tim Berners-Lee at CERN. HTML = Hypertext Markup Language, text format for describing layout, multimedia, hyperlinks
Mosaic : First browser created by Marc Andreessen at NCSA in 1993. Went on to found Netscape.
HTML, browsers spec continues to change today

## Slide 11: A Communications Model
Source
  generates data to be transmitted
Transmitter
  Converts data into transmittable signals
Transmission System
  Carries data
Receiver
  Converts received signal into data
Destination
  Takes incoming data

## Slide 12: Simplified Communications Model - Diagram

## Slide 13: Simplified Data Communications Model

## Slide 14: Key Communications Tasks
Transmission System Utilization
Interfacing
Signal Generation
Synchronization
Exchange Management
  Error detection and correction
  Flow control
Addressing and routing
Recovery
Message formatting
Security
Network Management

## Slide 15: Networking
Previous simplified model was Point to Point
Point to Point communication not usually practical
  Devices are too far apart
  Large set of devices would need impractical number of connections
Solution is a communications network
  Many different topologies, or ways to connect the network

## Slide 16: Types of Networks
Networks can be classified in many different ways. One of the most common is by geographic scope:
  Local Area Networks (LAN)
  Backbone Networks (BNs)
  Metropolitan Area Networks (MANs)
  Wide Area Networks (WANs)

## Slide 17: Types of Networks

## Slide 18: Types of Networks
Local Area Networks (LAN)
  A group of microcomputers of terminals located in the same general area and connected by a common circuit.
  Covers a clearly defined small area, such as within or between a few rooms or buildings.
  Generally support data rates of 10 to 100 million bits per second (Mbps).

## Slide 19: Types of Networks
Backbone Network (BN)
  A larger, central network connecting several LANs, other BNs, metropolitan area networks, and wide area networks.
  Typically span up to several miles.
  Generally supports data rates from 64 Kbps to 45 Mbps.
  Sometimes this term is also applied to WAN’s

## Slide 20: Types of Networks
Metropolitan Area Network (MAN)
  Connects LANs and BNs located in different areas to each other and to wide area networks.
  Typically span from 3 - 30 miles.
  Generally supports data rates of 100 to 1000 Mbps.

## Slide 21: Types of Networks
Wide Area Network (WAN)
  Connects BNs and MANs and are usually leased from inter-exchange carriers (IXC’s), i.e. common carriers
  Typically span hundreds or thousands of miles.
  Crossing public rights of way
  Generally supports data rates of 28.8 Kbps to 2 Gbps.

## Slide 22: Simplified Network Model

## Slide 23: How does the data travel?
When data may travel different paths in a network, there are currently two different approaches to implement this:
  Circuit switching
  Packet switching

## Slide 24: Circuit Switching
Dedicated end-to-end communications path established for the duration of the conversation
Path between the sender and receiver is called a circuit
Circuit also serves as a constant transmission rate for the duration of the connection – guaranteed constant rate
Might use multiplexing, where multiple devices share the same communications line
Example of circuit switching: telephone network, ISDN

## Slide 25: Packet Switching
Data may be sent out of sequence
Small chunks (packets) of data at a time
Packets passed from node to node between source and destination
Used for terminal to computer and computer to computer communications
Packet Switching examples: X.25, Frame Relay, TCP/IP

## Slide 26: Circuit vs. Packet Switching
Packet switching not suitable for real-time services?
But:
  Better sharing of bandwidth
    Consider statistical usage
  Simpler, more efficient, less costly
Trend toward packet switching
ATM: Asynchronous Transfer Mode, Packet switching, but allows constant data rate channel similar to circuit switching… we will examine it more later!

## Slide 27: Software and Protocols
LAN/WAN hardware can't solve all computer communication problems
  Sending data through raw hardware is awkward and inconvenient - doesn't match programming paradigms well
  Imagine reading a disk by having to write your own code each time to position the read/write head, seek, etc.
Network software provides a high-level interface to applications
  But this software for LAN and WAN systems is large and complicated
Layering is a structuring technique to organize networking software design and implementation

## Slide 28: Layers and Protocols
The software at each layer adheres to a protocol
A network protocol is a set of rules that specify the format and meaning of messages exchanged between computers across a network
  Format is sometimes called syntax
  Meaning is sometimes called semantics
Protocols are implemented by protocol software

## Slide 29: Protocol Suites
A set of related protocols that are designed for compatibility is called a protocol suite
Protocol suite designers:
  Analyze communication problem
  Divide problems into subproblems
  Design a protocol for each subproblem
A well-designed protocol suite
  Is efficient and effective - solves the problem without redundancy and makes best use of network capacity
  Allows replacement of individual protocols without changes to other protocols

## Slide 30: Example: Protocol Architecture
For example a file transfer problem might use three layers, each is independent with their own protocol
  File transfer application
    Transmits file transfer commands, e.g. “Send File X”
  Communication transport service layer
    Data integrity, break data into packets
  Network access layer
    Interface to hardware, addressing, routing
If multiple protocols at each layer, since they are independent, one could invoke other protocols!

## Slide 31: Example: Protocols in Simplified File Transfer App

## Slide 32: Example: Protocol Data Units (PDU)
At each layer, protocols are used to communicate
Control information is added to the packet of data at each layer
  Start with a packet at the Application Layer
  The Transport Layer adds its own header of control information to the packet
    Might even fragment a big packet into multiple little packets
    If so, must add sequence numbers, ID of sending application or there may be confusion if multiple apps, data arrives out of sequence
  The Network layer may in turn add its own header of control information to the Transport Layer packets
    E.g., addressing information

## Slide 33: Example: Operation of a Protocol Architecture

## Slide 34: TCP/IP Protocol Architecture
Developed by the US Defense Advanced Research Project Agency (DARPA) for its packet switched network (ARPANET)
TCP/IP are protocols in the suite; there are many other protocols as well
Used by the global Internet
  Open system, not proprietary (e.g. Appletalk, IPX/SPX, netbeui)
  Many vendors for the different layers of the stacks
No official model but a working one.
  Application layer
  Host to host or Transport layer
  Internet layer
  Network access layer or Data Link layer or Device layer
  Physical layer
Layers is a logical idea - can be ignored in implementation

## Slide 35: Application Layer
Support for user applications
  The application software used by the network user, allows the user to define what message are sent over the network.
e.g. HTTP, SMTP

## Slide 36: Transport Layer (TCP)
Takes the message generated by the application layer and performs these functions before passing them to the IP layer.
    1. Attaches application identifier (i.e. the port number)
    2. Splits data into packets for ordering of delivery
    3. Collects message accounting information that can be used to identify how many messages each user has sent and to track errors. This provides the reliable delivery of data.

## Slide 37: Internet Layer (IP)
Takes each packet generated by the TCP layer and performs the following functions before passing it to the Data Link / Network Access layer:
  Determines an address for the destination understood by the network
  Systems may be attached to different networks, provides routing functions from source to destination across multiple networks

## Slide 38: Device / Data Link / Network Access Layer
Takes the message generated by the IP layer and performs three functions before passing the message on the physical layer.
    1. It controls the physical layer by deciding when to transmit messages over the media.
    2. It formats the message by indicating where messages start and end, and which part is the address.
    3. It detects and corrects any errors that have occurred in the transmission of the message.

## Slide 39: Physical Layer
Physical interface between data transmission device (e.g. computer) and transmission medium or network. It transfers a series of electrical, radio, or light signals through the circuit from sender to receiver.
  Characteristics of transmission medium
  Signal levels
  Data rates
  etc.

## Slide 40: TCP/IP Layering
Application (ftp)
Transport (tcp)
Internet (ip)
Data Link (eth)
Physical (10BaseT)
Network
(Router up to
IP Layer)
Application (ftpd)
Transport (tcp)
Internet (ip)
Data Link (eth)
Physical (RF)

## Slide 41: Data Encapsulation
Network layer in this picture includes Transport and Internet Layers

## Slide 42: Some Protocols
Application Email (SMTP/POP) DNS Ping
Telnet/rlogin NFS traceroute
FTP SNMP
Web/HTTP RIP/Bootp
Transport TCP UDP
Internet IP / ICMP / IGMP
Data Link Ethernet / ARP
SLIP, PPP
Token Ring, Xmodem, HDLC

## Slide 43: Transport / Internet Layer
Remember that the layers are independent!

## Slide 44: Design of TCP/IP Stack
Layers in the protocol physically communicate either up or down the stack
  Transport layer talks to Internet and Application layer, never directly to the Physical layer
  Hides details of other layers
Layers in the protocol logically communicate with the peer layer of the recipient
  FTP source client talks to FTPD on recipient
  TCP source talks to remote endpoint TCP
  IP source talks to remote endpoint IP, maybe routers

## Slide 45: OSI Model
Open Systems Interconnection
Developed by the International Organization for Standardization (ISO)
Seven layers
A theoretical system delivered too late!
TCP/IP is the de facto standard

## Slide 46: OSI v TCP/IP
7
6
5
4
3
2
1

## Slide 47: The Importance of Standards
Standards are necessary in almost every business and public service entity.
The primary reason for standards is to ensure that hardware and software produced by different vendors can work together.
The use of standards makes it much easier to develop software and hardware that link different networks because software and hardware can be developed one layer at a time.

## Slide 48: The Standards Making Process
Two types of standards:
  Formal standards are developed by an official industry or government body.
  Defacto standards emerge in the marketplace and supported by several vendors, but have no official standing.

## Slide 49: The Standards Making Process
  Formal standardization process has three stages
  1. Specification stage: developing a nomenclature and identifying the problems to be addressed.
  2. Identification of choices stage: those working on the standard identify the various solutions and choose the optimum solution from among the alternatives.
  3. Acceptance, the most difficult stage: defining the solution and getting recognized industry leaders to agree on a single, uniform solution

## Slide 50: Telecommunications Standards Organizations
International Organization for Standards (ISO)
  Member of the ITU, makes technical recommendations about data communications interfaces.
ITU-T (formally CCITT)
ATM forum
Frame Relay forum
IETF

## Slide 51: Telecommunications Standards Organizations
International Telecommunications Union - Telecommunication Standardization Sector (ITU-TSS)
  Technical standard setting organization of the UN ITU. Formerly called the Consultative Committee on International Telegraph and Telephone (CCITT)
  Comprised of representatives of over 150 Postal Telephone and Telegraphs (PTTs), like AT&T, RBOCs, or common carriers.

## Slide 52: Other Standards Organizations
  American National Standards Institute (ANSI)
  Institute of Electrical and Electronics Engineers (IEEE)
  Electronic Industries Association (EIA)
  National Institute of Standards and Technology (NIST)
  National Exchange Carriers Association (NECA)
  Corporation for Open Systems (COS)
  Electronic Data Interchange -(EDI) of Electronic Data Interchange for Administration Commerce and Transport (EDIFACT).

## Slide 53: Some Standards
Application Layer
  HTTP, HTML, POP, MPEG, HTTPS
Network Layer
  TCP/IP, IPX/SPX
Data Link Layer
  802.3 Ethernet, Token Ring, PPP, X-modem, H.283
Physical Layer
  RS-232, IEEE CAT 5 Cable, V.90, V.34

## Slide 54: Standards
Required to allow for interoperability between equipment
Advantages
  Ensures a large market for equipment and software
  Allows products from different vendors to communicate
Disadvantages
  Freeze technology
  May be multiple standards for the same thing

## Slide 55: Probing The Internet: Apps
Two tools are common:
ping - sends message that is echoed by remote computer
  Arguments and behavior varies a bit between Windows/Unix
traceroute - reports path to remote computer
  Use tracert in Windows
Both tools are quite useful for rudimentary debugging of the network. We will examine both in more detail later, but first here is a look at their high-level usage.

## Slide 56: Ping Example
Sends packet to remote computer
Remote computer replies with echo packet
Local computer reports receipt of reply
May include round trip time
mazzy> ping beowulf.alaska.net
PING beowulf.alaska.net (209.112.130.8): 56 data bytes
64 bytes from 209.112.130.8: icmp_seq=0 ttl=237 time=140.3 ms
64 bytes from 209.112.130.8: icmp_seq=1 ttl=237 time=139.6 ms
64 bytes from 209.112.130.8: icmp_seq=2 ttl=237 time=151.0 ms
64 bytes from 209.112.130.8: icmp_seq=3 ttl=237 time=137.0 ms
--- beowulf.alaska.net ping statistics ---
5 packets transmitted, 4 packets received, 20% packet loss
round-trip min/avg/max = 137.0/141.9/151.0 ms

## Slide 57: Traceroute Example
Sends series of packets along path to destination
  Each successive packet identifies next router along path
  Packets have a “Time To Live” option that is incremented
  Uses expanding ring search
Reports list of packets
mazzy> traceroute styx.gci.net
traceroute to styx.gci.net (208.138.129.15), 30 hops max, 46 byte packets
1 137.229.114.101 (137.229.114.101) 0.896 ms 0.737 ms 0.694 ms
2 swa-7206-1.uaa.alaska.edu (137.229.101.2) 1.540 ms 0.836 ms 0.896 ms
3 121-village-net.gci.net (209.165.156.121) 1.589 ms 2.062 ms 1.574 ms
4 * styx.gci.net (208.138.129.15) 5.530 ms *
From UAA, try a traceroute to www.alaska.net!

## Slide 58: Protocols in Ping/Traceroute
What protocols were involved?
  At a high level…
  Ping : The app sent data in some format that was recognized by the receiver. The receiver was running a program whose responsibility was to echo the packet back.
  Traceroute : The app sent data with increasing TTL fields. There must be some receiver program that will report back “Your packet died here”

## Slide 59: Discussion Problem: Email Delivery
Say you want to devise a protocol that can receive data from a client and eventually pass it on to the recipient (i.e. sendmail).
What should be in this protocol? What layer are we talking about? Ideas for defining it? We will look at email a bit more in a homework exercise.