## Slide 1: Limits on ILP

## Slide 2: Achieving Parallelism
Techniques
  Scoreboarding / Tomasulo’s Algorithm
  Pipelining
  Speculation
  Branch Prediction
But how much more performance could we theoretically get? How much ILP exists?
How much more performance could we realistically get?

## Slide 3: Methodology
Assume an ideal (and impractical) processor
Add limitations one at a time to measure individual impact
Consider ILP limits on a hypothetically practical processor
Analysis performed on benchmark programs with varying characteristics

## Slide 4: Hardware Model – Ideal Machine
Remove all limitations on ILP
  Register renaming
    Infinite number of registers available, eliminating all WAW and WAR hazards
  Branch prediction
    Perfect, including targets for jumps
  Memory address alias analysis
    All addresses known exactly, a load can be moved before a store provided that the addresses are not identical
  Perfect caches
    All memory accesses take 1 clock cycle
  Infinite resources
    No limit on number of functional units, buses, etc.

## Slide 5: Ideal Machine
All control dependencies removed by perfect branch prediction
All structural hazards removed by infinite resources
All that remains are true data dependencies (RAW) hazards
All functional unit latencies: one clock cycle
  Any dynamic instruction can execute in the cycle after its predecessor executes
Initially we assume the processor can issue an unlimited number of instructions at once looking arbitrarily far ahead in the computation

## Slide 6: Experimental Method
Programs compiled and optimized with standard MIPS optimizing compiler
The programs were instrumented to produce a trace of instruction and data references over the entire execution
Each instruction was subsequently re-scheduled as early as the true data dependencies would allow
  No control dependence

## Slide 7: Benchmark Programs – SPECINT92

## Slide 8: ILP on the Ideal Processor

## Slide 9: How close could we get to the ideal?
The perfect processor must do the following:
  Look arbitrarily far ahead to find a set of instructions to issue, predicting all branches perfectly
  Rename all registers to avoid WAR and WAW hazards
  Resolve data dependencies
  Resolve memory dependencies
  Have enough functional units for all ready instructions

## Slide 10: Limiting the Instruction Window
Limit window size to n (no longer arbitrary)
  Window = number of instructions that are candidates for concurrent execution in a cycle
Window size determines
  Instruction storage needed within the pipeline
  Maximum issue rate
  Number of operand comparisons needed for dependence checking is O(n2)
    To try and detect dependences among 2000 instructions would require some 4 million comparisons
    Issuing 50 instructions requires 2450 comparisons

## Slide 11: Effect of Reduced Window Size
Notes: Best window size today around 200

## Slide 12: Effect of Reduced Window Size

## Slide 13: Effect of Reduced Window Size
Integer programs do not have as much parallelism as floating point programs
  Scientific nature of the program
Highly dependent on loop-level parallelism
  Instructions that can execute in parallel across loop iterations cannot be found with small window sizes without compiler help
From now on, assume:
  Window size of 2000
  Maximum of 64 instructions issued per cycle

## Slide 14: Effects of Branch Prediction
So far, all branch outcomes are known before the first instruction executes
  This is difficult to achieve in hardware or software
Consider 5 alternatives
  Perfect
  Tournament predictor
    (2,2) prediction scheme with 8K entries
  Standard (non-correlating) 2-bit predictor
  Static (profile-based)
  None (parallelism limited to within current basic block)
No penalty for mispredicted branches except for unseen parallelism

## Slide 15: Branch Prediction Accuracy
Notes: I think not really 100% on tomcatv

## Slide 16: Effects of Branch Prediction

## Slide 17: Effects of Branch Prediction

## Slide 18: Branch Prediction
Accurate prediction is critical to finding ILP
Loops are easy to predict
Independent instructions are separated by many branches in the integer programs and doduc
From now on, assume tournament predictor
  Also assume 2K jump and return predictors

## Slide 19: Effect of Finite Registers
What if we no longer have infinite registers? Might have WAW or WAR hazards
Alpha 21264 had 41 gp and integer renaming registers
IBM Power5 has 88 fp and integer renaming registers

## Slide 20: Effect of Renaming Registers

## Slide 21: Effects of Renaming Registers

## Slide 22: Renaming Registers
Not a big difference in integer programs
  Already limited by branch prediction and window size, not that many speculative paths where we run into renaming problems
Many registers needed to hold live variables for the more predictable floating point programs
Significant jump at 64
We will assume 256 integer and FP registers available for renaming

## Slide 23: Imperfect Alias Analysis
Memory can have dependencies too, so far assumed they can be eliminated
So far, memory alias analysis has been perfect
Consider 3 models
  Global/stack perfect: idealized static program analysis (heap references are assumed to conflict)
  Inspection: a simpler, realizable compiler technique limited to inspecting base registers and constant offsets
  None: all memory references are assumed to conflict

## Slide 24: Effects of Imperfect Alias Analysis
Notes: No heap references for fpppp and tomcatv

## Slide 25: Effects of Imperfect Alias Analysis

## Slide 26: Memory Disambiguation
Fpppp and tomcatv use no heap so perfect with global/stack perfect assumption
  Perfect analysis here better by a factor of 2, implies there are compiler analysis or dynamic analysis to obtain more parallelism
Has big impact on amount of parallelism
Dynamic memory disambiguation constrained by
  Each load address must be compared with all in-flight stores
  The number of references that can be analyzed each clock cycle
  The amount of load/store buffering determines how far a load/store instruction can be moved

## Slide 27: What is realizable?
If our hardware improves, what may be realizable in the near future?
  Up to 64 instruction issues per clock (roughly 10 times the issue width in 2005)
  A tournament predictor with 1K entries and a 16 entry return predictor
  Perfect disambiguation of memory references done dynamically (ambitious but possible if window size is small)
  Register renaming with 64 int and 64 fp registers

## Slide 28: Performance on Hypothetical CPU

## Slide 29: Performance on Hypothetical CPU

## Slide 30: Hypothetical CPU
Ambitious/impractical hardware assumptions
  Unrestricted issue (particularly memory ops)
  Single cycle operations
  Perfect caches
Other directions
  Data value prediction and speculation
    Address value prediction and speculation
  Speculation on multiple paths
  Simpler processor with larger cache and higher clock rate vs. more emphasis on ILP with a slower clock and smaller cache