## Slide 1: CUDA
More on Blocks/Threads

## Slide 2: Debugging Using the Device Emulation Mode
An executable compiled in device emulation mode (nvcc -deviceemu) runs completely on the host using the CUDA runtime
  No need of any device and CUDA driver
  Each device thread is emulated with a host thread
Running in device emulation mode, one can:
  Use host native debug support (breakpoints, inspection, etc.)‏
    Compile with –g –G debug with: cuda-gdb <program name>
  Access any device-specific data from host code and vice-versa
  Call any host function from device code (e.g. printf) and vice-versa
  Detect deadlock situations caused by improper usage of __syncthreads
X
Notes: There is a cuPrintf library but need developer access

## Slide 3: Device Emulation Mode Pitfalls
Emulated device threads execute sequentially, so simultaneous accesses of the same memory location by multiple threads could produce different results.
Dereferencing device pointers on the host or host pointers on the device can produce correct results in device emulation mode, but will generate an error in device execution mode

## Slide 4: Floating Point
Results of floating-point computations will slightly differ because of:
  Different compiler outputs, instruction sets
  Use of extended precision for intermediate results
    There are various options to force strict single precision on the host

## Slide 5: CUDA Thread Block
All threads in a block execute the same kernel program (SPMD)
Programmer declares block:
  Block size 1 to 512 concurrent threads
  Block shape 1D, 2D, or 3D
  Block dimensions in threads
Threads have thread id numbers within block
  Thread program uses thread id to select work and address shared data
Threads in the same block share data and synchronize while doing their share of the work
Threads in different blocks cannot cooperate
  Each block can execute in any order relative to other blocs!
  End kernel and go back to host to enforce order
CUDA Thread Block
Thread Id #: 0 1 2 3 … m
Thread program
Courtesy: John Nickolls, NVIDIA
Notes: Frustrating blocks can’t synchronize but part of scalability

## Slide 6: G80 CUDA mode – A Review
Processors execute computing threads
New operating mode/HW interface for computing
Load/store
Global Memory
Thread Execution Manager
Input Assembler
Host
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Texture
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Parallel Data Cache
Load/store
Load/store
Load/store
Load/store
Load/store

## Slide 7: Transparent Scalability
Hardware is free to assigns blocks to any processor at any time
  A kernel scales across any number of parallel processors
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Kernel grid
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Device
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Each block can execute in any order relative to other blocks.
time

## Slide 8: G80 Example: Executing Thread Blocks
Threads are assigned to Streaming Multiprocessors in block granularity
  Up to 8 blocks to each SM as resource allows
  SM in G80 can take up to 768 threads
    Could be 256 (threads/block) * 3 blocks
    Or 128 (threads/block) * 6 blocks, etc.
Threads run concurrently
  SM maintains thread/block id #s
  SM manages/schedules thread execution
t0 t1 t2 … tm
Blocks
SP
Shared
Memory
MT IU
SP
Shared
Memory
MT IU
t0 t1 t2 … tm
Blocks
SM 1
SM 0

## Slide 9: G80 Example: Thread Scheduling
Each Block is executed as 32-thread Warps
  An implementation decision, not part of the CUDA programming model
  Warps are scheduling units in SM
If 3 blocks are assigned to an SM and each block has 256 threads, how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 1 Warps
Block 2 Warps
SP
SP
SP
SP
SFU
SP
SP
SP
SP
SFU
Instruction Fetch/Dispatch
Instruction L1
Streaming Multiprocessor
Shared Memory
…
t0 t1 t2 … t31
…
Block 1 Warps
Notes: 32 threads would run efficiently in a block

## Slide 10: G80 Example: Thread Scheduling (Cont.)
SM implements zero-overhead warp scheduling
  At any time, only one of the warps is executed by SM
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution on a prioritized scheduling policy
  All threads in a warp execute the same instruction when selected
Notes: A little different than SMP, overlapping memory delays accesses across warps; like scoreboarding; shows blocks can finish in any order

## Slide 11: G80 Block Granularity Considerations
For Matrix Multiplication using multiple blocks, should I use 8X8, 16X16 or 32X32 threads per block?
  For 8X8, we have 64 threads per Block. Since each SM can take up to 768 threads, there are 12 Blocks. However, each SM can only take up to 8 Blocks, only 512 threads will go into each SM!
  For 16X16, we have 256 threads per Block. Since each SM can take up to 768 threads, it can take up to 3 Blocks and achieve full capacity unless other resource considerations overrule.
  For 32X32, we have 1024 threads per Block. Not even one can fit into an SM!
Our earlier Julia fractal implementation not as good as it could have been; why not?
Notes: Julia fractal program could have been improved if split into blocks, where each block does a 16x16 pixel area with 256 threads
If not an even number of blocks, have a block with a smaller number of threads (if statement to check for border case)

## Slide 12: Sub-Blocks and Threads
P1,0
P0,0
P0,1
P2,0
P3,0
P1,1
P0,2
P2,2
P3,2
P1,2
P3,1
P2,1
P0,3
P2,3
P3,3
P1,3
Block(0,0)
Block(1,0)
Block(1,1)
Block(0,1)
TILE_WIDTH = 2
Mapping to row and column
Row in P =
blockIdx.y * TILE_WIDTH + threadIdx.y
Column in P =
blockIdx.x * TILE_WIDTH + threadIdx.x
Then map to 1D array
P[Row * WIDTH + Column] = Value
blockDim.x

## Slide 13: Example
Matrix Mul program:
#define DIM 4
__global__ void MatrixGenerate(int* M, int* N, int* P, int width)
{
int row = blockIdx.y * blockDim.x + threadIdx.y;
int col = blockIdx.x * blockDim.x + threadIdx.x;
P[row * width + col] = (row + col);
}
dim3 blocks(DIM/2, DIM/2);
dim3 threads(DIM/2, DIM/2);
MatrixGenerate<<<blocks,threads>>>(dev_m, dev_n, dev_p, DIM);

## Slide 14: Improved Julia Fractal
Change block/thread size to better utilize thread support per SM
#define DIM 3008 // 16*188
__global__ void kernel(char *ptr)
{
int row = blockIdx.y * blockDim.x + threadIdx.y;
int col = blockIdx.x * blockDim.x + threadIdx.x;
int offset = col + row * DIM;
ptr[offset] = julia(row,col);
}
dim3 blocks(188,188);
dim3 threads(16,16);
kernel<<<blocks,threads>>>(dev_charmap);

## Slide 15: Long Vectors
Using 1 block, limited to 512 threads
Maximum of 65535 blocks
If you want to operate on something longer than 65535 even if it’s 1D then we have to combine blocks and threads
Thread 0 | Thread 1 | Thread 2 | Thread 3 | Thread 4
Thread 0 | Thread 1 | Thread 2 | Thread 3 | Thread 4
Thread 0 | Thread 1 | Thread 2 | Thread 3 | Thread 4
Thread 0 | Thread 1 | Thread 2 | Thread 3 | Thread 4
Block 0
Block 1
Block 2
Block 3
…
Block 32000
1D array index = (blockIdx.x * blockDim.x) + threadIdx.x = 0 to 32000*5+4 = 160,004

## Slide 16: Arbitrarily Long Vectors
The limit is 512 threads per block, so there is a failure if the vector is of size N and N/512 > 65535
  N > 65535*512 = 33,553,920 elements
  Pretty big but we could have the capacity for up to 4GB
Solution
  Have to assign range of data values to each thread instead of each thread only operating on one value

## Slide 17: Some Additional API Features

## Slide 18: Language Extensions: Built-in Variables
dim3 gridDim;
  Dimensions of the grid in blocks (gridDim.z unused)
dim3 blockDim;
  Dimensions of the block in threads
dim3 blockIdx;
  Block index within the grid
dim3 threadIdx;
  Thread index within the block

## Slide 19: Common Runtime Component: Mathematical Functions
pow, sqrt, cbrt, hypot
exp, exp2, expm1
log, log2, log10, log1p
sin, cos, tan, asin, acos, atan, atan2
sinh, cosh, tanh, asinh, acosh, atanh
ceil, floor, trunc, round
Etc.
  When executed on the host, a given function uses the C runtime implementation if available
  These functions are only supported for scalar types, not vector types

## Slide 20: Device Runtime Component: Mathematical Functions
Some mathematical functions (e.g. sin(x)) have a less accurate, but faster device-only version (e.g. __sin(x))
  __pow
  __log, __log2, __log10
  __exp
  __sin, __cos, __tan

## Slide 21: Host Runtime Component
Provides functions to deal with:
  Device management (including multi-device systems)
  Memory management
  Error handling
Initializes the first time a runtime function is called
A host thread can invoke device code on only one device
  Multiple host threads required to run on multiple devices

## Slide 22: Device Runtime Component: Synchronization Function
void __syncthreads();
Synchronizes all threads in a block
Once all threads have reached this point, execution resumes normally
Used to avoid RAW / WAR / WAW hazards when accessing shared or global memory
Allowed in conditional constructs only if the conditional is uniform across the entire thread block
Notes: Atomic Operations?