## Slide 1: Hardware-Based Speculation

## Slide 2: Exploiting More ILP
Branch prediction reduces stalls but may not be sufficient to generate the desired amount of ILP
One way to overcome control dependencies is with speculation
  Make a guess and execute program as if our guess is correct
  Need mechanisms to handle the case when the speculation is incorrect
Can do some speculation in the compiler
  We saw this previously with reordered / duplicated instructions around branches

## Slide 3: Hardware-Based Speculation
Extends the idea of dynamic scheduling with three key ideas:
  Dynamic branch prediction
  Speculation to allow the execution of instructions before control dependencies are resolved
  Dynamic scheduling to deal with scheduling different combinations of basic blocks
    What we saw earlier was within a basic block
Modern processors started using speculation around the introduction of the PowerPC 603, Intel Pentium II and extend Tomasulo’s approach to support speculation

## Slide 4: Speculating with Tomasulo
Separate execution from completion
  Allow instructions to execute speculatively but do not let instructions update registers or memory until they are no longer speculative
Instruction Commit
  After an instruction is no longer speculative it is allowed to make register and memory updates
Allow instructions to execute and complete out of order but force them to commit in order
Add a hardware buffer, called the reorder buffer (ROB), with registers to hold the result of an instruction between completion and commit
  Acts as a FIFO queue in order issued

## Slide 5: Original Tomasulo Architecture

## Slide 6: Tomasulo and Reorder Buffer
Sits between Execution and Register File
Source of operands
In this case integrated with Store buffer
Reservation stations use ROB slot as a tag
Instructions commit at head of ROB FIFO queue
  Easy to undo speculated instructions on mispredicted branches or on exceptions

## Slide 7: ROB Data Structure
Instruction Type Field
  Indicates whether the instruction is a branch, store, or register operation
Destination Field
  Register number for loads, ALU ops, or memory address for stores
Value Field
  Holds the value of the instruction result until instruction commits
Ready Field
  Indicates if instruction has completed execution and the value is ready

## Slide 8: Instruction Execution
Issue: Get an instruction from the Instruction Queue
  If the reservation station and the ROB has a free slot (no structural hazard), issue the instruction to the reservation station and the ROB, send operands to the reservation station if available in the register file or the ROB. The allocated ROB slot number is sent to the reservation station to use as a tag when placing data on the CDB.
Execution: Operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result
Write result: Finish execution (WB)
  Write on CDB to all awaiting units and to the ROB using the tag; mark reservation station available
Commit: Update register or memory with the ROB result
  When an instruction reaches the head of the ROB and results are present, update the register with the result or store to memory and remove the instruction from the ROB
  If an incorrectly predicted branch reaches the head of the ROB, flush the ROB, and restart at the correct successor of the branch
Blue text = Change from Tomasulo

## Slide 9: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
State
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
 |  |  |  | ROB7
 |  |  |  | ROB6
 |  |  |  | ROB5
 |  |  |  | ROB4
 |  |  |  | ROB3
 |  |  |  | ROB2
F0 |  | LD F0, 10(R2) | I | ROB1
Dest
1 | 10+R2
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 10: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
State
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
 |  |  |  | ROB7
 |  |  |  | ROB6
 |  |  |  | ROB5
 |  |  |  | ROB4
 |  |  |  | ROB3
 |  |  |  | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
Dest
1 | 10+R2
Notes: Cache miss on Load, long execution time

## Slide 11: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
 |  |  |  | ROB7
 |  |  |  | ROB6
 |  |  |  | ROB5
 |  |  |  | ROB4
 |  |  |  | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
2 | ADDD | R(F4),1
Dest
1 | 10+R2
State
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 12: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
 |  |  |  | ROB7
 |  |  |  | ROB6
 |  |  |  | ROB5
 |  |  |  | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
2 | ADDD | R(F4),1
Dest
3 | MULD | 2,R(F6)
1 | 10+R2
State
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 13: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
 |  |  |  | ROB7
F0 |  | ADDD F0,F4,F6 | I | ROB6
F4 |  | LD F4,0(R3) | E | ROB5
-- |  | BNE F0, 0, L | I | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
2 | ADDD | R(F4),1
6 | ADDD | 5,R(F6)
Dest
3 | MULD | 2,R(F6)
1 | 10+R2
5 | 0+R3
State
Notes: Suppose BNE issues but is stalled waiting for operands
Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 14: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | ROB5 | ST F4, 0(R3) | I | ROB7
F0 |  | ADDD F0,F4,F6 | I | ROB6
F4 |  | LD F4,0(R3) | E | ROB5
-- |  | BNE F0, 0, L | I | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
2 | ADDD | R(F4),1
6 | ADDD | 5,R(F6)
Dest
3 | MULD | 2,R(F6)
1 | 10+R2
5 | 0+R3
State
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 15: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 |  | ADDD F0,F4,F6 | I | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | I | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
2 | ADDD | R(F4),1
6 | ADDD | V1,R(F6)
Dest
3 | MULD | 2,R(F6)
1 | 10+R2
State
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 16: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 |  | ADDD F0,F4,F6 | E | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | I | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
2 | ADDD | R(F4),1
Dest
3 | MULD | 2,R(F6)
1 | 10+R2
State
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 17: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | I | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 |  | LD F0, 10(R2) | E | ROB1
2 | ADDD | R(F4),1
Dest
3 | MULD | 2,R(F6)
1 | 10+R2
State
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 18: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | I | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | I | ROB2
F0 | V3 | LD F0, 10(R2) | W | ROB1
2 | ADDD | R(F4),V3
Dest
3 | MULD | 2,R(F6)
State
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 19: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | E | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 |  | ADDD F10,F4,F0 | E | ROB2
F0 | V3 | LD F0, 10(R2) | C | ROB1
Dest
3 | MULD | 2,R(F6)
State
F0=V3

## Slide 20: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | W | ROB4
F2 |  | MULD F2,F10,F6 | I | ROB3
F10 | V4 | ADDD F10,F4,F0 | W | ROB2
F0 | V3 | LD F0, 10(R2) | C | ROB1
Dest
3 | MULD | V4,R(F6)
State
F0=V3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 21: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | W | ROB4
F2 |  | MULD F2,F10,F6 | E | ROB3
F10 | V4 | ADDD F10,F4,F0 | C | ROB2
F0 | V3 | LD F0, 10(R2) | C | ROB1
Dest
State
F0=V3
F10=V4
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 22: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | W | ROB4
F2 | V5 | MULD F2,F10,F6 | W | ROB3
F10 | V4 | ADDD F10,F4,F0 | C | ROB2
F0 | V3 | LD F0, 10(R2) | C | ROB1
Dest
State
F0=V3
F10=V4
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 23: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | W | ROB4
F2 | V5 | MULD F2,F10,F6 | C | ROB3
F10 | V4 | ADDD F10,F4,F0 | C | ROB2
F0 | V3 | LD F0, 10(R2) | C | ROB1
Dest
State
F0=V3
F10=V4
F2=V5
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 24: Tomasulo With ROB
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
Dest
Oldest
Newest
From
Memory
Dest
Reorder Buffer
Registers
[R3] | V1 | ST F4, 0(R3) | W | ROB7
F0 | V2 | ADDD F0,F4,F6 | W | ROB6
F4 | V1 | LD F4,0(R3) | W | ROB5
-- |  | BNE F0, 0, L | C | ROB4
F2 | V5 | MULD F2,F10,F6 | C | ROB3
F10 | V4 | ADDD F10,F4,F0 | C | ROB2
F0 | V3 | LD F0, 10(R2) | C | ROB1
Dest
State
F0=V3
F10=V4
F2=V5
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 25: Avoiding Memory Hazards
A store only updates memory when it reaches the head of the ROB
  Otherwise WAW and WAR hazards are possible
  By waiting to reach the head memory is updated in order and no earlier loads or stores can still be pending
If a load accesses a memory location written to by an earlier store then it cannot perform the memory access until the store has written the data
  Prevents RAW hazard through memory

## Slide 26: Reorder Buffer Implementation
In practice
  Try to recover as early as possible after a branch is mispredicted rather than wait until branch reaches the head
  Performance in speculative processors more sensitive to branch prediction
    Higher cost of misprediction
Exceptions
  Don’t recognize the exception until it is ready to commit
  Could try to handle exceptions as they arise and earlier branches resolved, but more challenging